## Slide 1
TECHNION · COURSE 00460882 · HW/SW CO-DESIGN
Benchmark Optimization
& Hardware Acceleration
Profiling · SW Optimization · RTL Design
nbody (SW only) · pyflate (SW + HW accelerator)
BY
Feras Hosen · Badir Zoabi

## Slide 2
Agenda
28 SLIDES · ~24 MIN
PART 1 — SETUP
03 HW/SW co-design & the loop
04 Two benchmarks & why
05 Methodology & toolchain
PART 2 — NBODY (SW ONLY)
06 What it simulates
07 Profile → bottleneck + table
08 Inner loop math
09 The sqrt idea that failed
10 Real fix: scalar locals
11 Result: 1.58× / ~37%
PART 3 — PYFLATE (SW + HW)
12 What it does
13 Profile → bottlenecks + table
14 Decompression pipeline
15 Optimizations OPT-1/2/3
16 Result: 1.50× / ~33%
PART 4 — HARDWARE (PYFLATE · 2 COMPONENTS)
17 Co-design rule
18 Accelerator block diagram
19 HW/SW interface & trade-offs
20 MTF unit — 2nd component
21 MTF internal block diagram
22 FSM deep-dive & RTL snippet
23 Amdahl: (A) ~1.77× → (A+B) ~2.16×
24 TB PASS · both components
25 Results summary & takeaways
26 Git repo & documentation

## Slide 3
HW/SW CO-DESIGN
What is
Co-design?
Jointly designing software and hardware to maximize system performance — neither in isolation.
🔬
Measure
Profile the real bottleneck — not the assumed one
↓
⚙️
Optimize SW
Cut interpreter overhead, allocation churn, better algorithms
↓
💾
Accelerate HW
Offload the irreducible hot kernel to silicon
SUCCESS CRITERION
≥7%
wall-clock speedup on pyperformance
THIS PROJECT
nbody → SW only (1.58× / ~37%)
pyflate → SW + HW accelerator (1.50× SW, ~2.16× HW est.)

## Slide 4
TWO BENCHMARKS · TWO PROFILES
BENCHMARK 1 — SW ONLY
nbody
pyperformance · nbody
Compute-bound
→ Solar system gravitational dynamics
→ O(N²) pairs · 20,000 steps · pure Python
→ State in Python lists (mutable subscripts)
Bottleneck: interpreter overhead + list subscripting
BENCHMARK 2 — SW + HW
pyflate
pyperformance · pyflate
Bit/Control-bound
→ Pure-Python bzip2/gzip decompressor
→ Bit reader → Huffman → MTF → BWT
→ Millions of tiny Python calls per decode
Bottleneck: object alloc churn · MTF · bit reads · Huffman scan
Both pure Python — no C extensions, no NumPy. All overhead is interpreter-visible and measurable.
Complementary profiles: FP-heavy (nbody) vs. allocation/control-heavy (pyflate) → two distinct optimization stories.

## Slide 5
MEASURE → OPTIMIZE → ACCELERATE
Methodology & Toolchain
⏱️
pyperformance + pyperf
Standardized runner · wall-clock timing · 60 values/side · mean ± std dev · compare_to for before/after ratio
🔥
perf + FlameGraph
perf record -F 999 -g on python3-dbg · call-stack sampling · Brendan Gregg's FlameGraph · visual hotspot ID
🖥️
QEMU guest
Course "jammy" Ubuntu image · software CPU emulation · absolute times inflated vs. bare metal — ratios are valid (both sides same guest)
🔌
Icarus Verilog
RTL simulation · iverilog -g2012 · self-checking testbench · pyflate Huffman engine passes
✅
Success bar: ≥7% wall-clock speedup on ≥2 benchmarks
Measured with pyperf compare_to · n=60 · inside QEMU guest

## Slide 6
nbody — Solar System Simulation
Simulates the gravitational dynamics of the outer solar system — Sun + 4 gas giants — over 20,000 timesteps.
Bodies & data structures
5 bodies · each is a Python list [pos_list, vel_list, mass] · positions/velocities are 3-element mutable lists
Algorithm
Brute-force O(N²) · 10 pairs · symplectic-Euler integrator · 20,000 steps · no libraries beyond math.sqrt
Correctness oracle
Final system energy printed to 9 decimals: -0.169089263 — must be identical before/after
WHY IT'S A GOOD BENCHMARK
Deterministic · pure arithmetic · no I/O · energy checksum validates correctness · representative scientific computing workload

## Slide 7
LINUX PERF · PYTHON3-DBG · TOP FUNCTIONS
nbody — Profiling
FUNCTION | SELF % | WHAT IT MEANS
_PyEval_EvalFrameDefault | 35.0% | Bytecode dispatch — the interpreter loop
PyFloat_FromDouble | 7.3% | Boxing a new float per arithmetic result
binary_op1 / float_dealloc | 5.0 / 4.6% | Op dispatch + float object teardown
PyNumber_AsSsize_t | 3.7% | List index resolution (v1[0], v1[1], …)
__ieee754_pow_sse2 | 2.5% | ** -1.5 power op — looks tempting
float_mul / float_add / float_sub | ~1.5–2.3% | Actual FP arithmetic — barely visible
list_ass_subscript | 2.0% | v1[0] -= … list-subscript writes
Key: FP ops each only 1.5–2.5%. Interpreter + object overhead is 35%+.
sqrt swap: pow=2.5% → max saving 2.5% → got ~0–1.5%.
nbody original — flame graph

## Slide 8
O(N²) PAIRS · PER-PAIR COMPUTATION
nbody — The Inner Loop
THE HOT LOOP — ORIGINAL CODE
for (((x1,y1,z1),v1,m1), ((x2,y2,z2),v2,m2)) in pairs: dx = x1-x2; dy = y1-y2; dz = z1-z2 d2 = dx*dx + dy*dy + dz*dz mag = dt * (d2 ** -1.5) # ← power op b2m = m2*mag; b1m = m1*mag v1[0] -= dx*b2m # BINARY_SUBSCR v1[1] -= dy*b2m # BINARY_SUBSCR v1[2] -= dz*b2m # BINARY_SUBSCR v2[0] += dx*b1m # BINARY_SUBSCR v2[1] += dy*b1m # BINARY_SUBSCR v2[2] += dz*b1m # BINARY_SUBSCR
3× subtract
3× multiply (d²)
1× pow(-1.5)
4× multiply
6× subscript read + write (BINARY_SUBSCR + STORE_SUBSCR)
WHAT PYTHON DOES PER SUBSCRIPT
v1[0] -= dx*b2m
① LOAD_FAST v1 → pointer to list object
② LOAD_CONST 0 → integer object
③ BINARY_SUBSCR → dict lookup + bounds check
④ compute dx*b2m
⑤ BINARY_OP subtract
⑥ STORE_SUBSCR → type check + refcount update
Per pair: ~60+ bytecodes
6 subscript writes × ~6 bytecodes each, plus unpacking, arithmetic dispatch, float boxing/unboxing. The math is cheap. The interpreter tax is not.

## Slide 9
HYPOTHESIS — INCORRECT
The sqrt Idea
That Failed
"The inner loop uses (dx²+dy²+dz²) ** (-1.5) — a general power op. Replace it with a hardware sqrt: dt / (d2 * sqrt(d2)). Should be much faster."
MEASURED SPEEDUP
~1%
well below the 7% bar
Why it didn't work
pow is only 2.5% of runtime. Optimizing it can never move the needle — Amdahl's Law.
What the profile said
35% interpreter dispatch + list subscripting. That's the real target.
Lesson: measure, don't assume
The profiler told us the truth. We tried the intuitive fix first, measured it, found it useless, then went back to the data. That's the right process.

## Slide 10
SOFTWARE REGISTER ALLOCATION
nbody — Real Fix: Scalar Locals
BEFORE — LIST SUBSCRIPTS EVERY STEP
for (((x1,y1,z1),v1,m1), ((x2,y2,z2),v2,m2)) in pairs: dx = x1-x2; dy = y1-y2; dz = z1-z2 mag = dt * (d2 ** -1.5) v1[0] -= dx*b2m # BINARY_SUBSCR+STORE_SUBSCR v1[1] -= dy*b2m # ×3 per body, ×10 pairs v1[2] -= dz*b2m
v1[0] : find list → bounds-check index → load float → compute → store back
AFTER — SCALAR LOCALS, READ/WRITE ONCE
x0,y0,z0 = S[0][0] # read ONCE before loop vx0,vy0,vz0 = S[0][1] for _ in range(n): dx = x0-x1; dy = y0-y1; dz = z0-z1 mag = dt * (d2 ** -1.5) vx0 -= dx*b1 # LOAD_FAST — direct C slot vy0 -= dy*b1 # no list lookup at all S[0][1][:] = [vx0,vy0,vz0] # write ONCE after
Local slot vs list indexing, ×millions → ~37% faster
Why it works
LOAD_FAST = direct C array slot. BINARY_SUBSCR = dict lookup + type check + refcount. ~3× cheaper per access, across millions of iterations.
The analogy
Software "register allocation" — keep the hot working set in fast local slots instead of chasing pointers into heap list objects.
Correctness
Same math, same output. Energy checksum -0.169089263 identical to 9 decimals.

## Slide 11
WALL-CLOCK SPEEDUP
~37%
1.58× · 3.93 s → 2.50 s (n=60)
vs. 7% threshold
5.2× above target ✓
0%
7% bar
37%
BEFORE VS. AFTER
METRIC | BEFORE | AFTER
Wall-clock | 3.93 s ± 0.38 s | 2.50 s ± 0.22 s
Speedup | 1.00× | 1.58×
Key bytecode | BINARY_SUBSCR | LOAD_FAST
Energy checksum | -0.169089263 | -0.169089263 ✓
nbody optimized — flame graph (hotspot visibly narrower)

## Slide 12
pyflate — Pure-Python Decompressor
A complete bzip2 and gzip decompressor written entirely in Python — no C extensions. Every bit operation is visible to the interpreter.
What it decompresses
Fixed embedded interpreter.tar.bz2 (~66 KB compressed → 399,360 bytes). Checks MD5 of output.
Decompression pipeline
Bit reader → Canonical Huffman decode → Move-To-Front (MTF) → Run-Length decode → Inverse BWT
Why it's slow
Python does the bit/byte work the C library normally does. Millions of tiny calls, list allocations, and linear scans — all through the interpreter.
CONTRAST WITH NBODY
nbody: one tight arithmetic loop · pyflate: deep call stack, bit manipulation, branchy decode logic, heavy allocation churn

## Slide 13
CPROFILE SELF-TIME · ORIGINAL DECODER · ALL TOP FUNCTIONS
pyflate — Profiling
FUNCTION | SELF % | BUCKET | WHAT IT DOES
decode_huffman_block | ~23.4% | stays in SW | Block loop control / MTF dispatch
find_next_symbol | 15.85% | Huffman (A) | Linear scan of code table per symbol
readbits | 10.32% | Bit-read (A) | Read N bits from the stream
move_to_front | 10.30% | MTF (B) | 4 new list allocs per symbol
snoopbits | 9.55% | Bit-read (A) | Peek at bits without consuming
_mask / bwt_reverse / bwt_transform | 5.8 / 4.2 / 3.6% | stays in SW | Bit-mask helper / inverse BWT / BWT helper
_read / _more / needbits | 3.3 / 3.1 / 1.5% | Bit-read (A) | Internal bit-stream helpers
(A) 43.55%
(B) 10.30%
(A+B) 53.85% → ~2.16×
SW ~46% → next stage
pyflate baseline — before
pyflate optimized — after

## Slide 14
BZIP2 DECODE PATH · STAGE BY STAGE
pyflate — Decompression Pipeline
🔥 HOT
Bit Reader
RBitfield
reads 1 byte
at a time via
file object
27.70% of runtime
→
🔥 HOT
Huffman Decode
find_next_symbol
linear scan of
code table
per symbol
15.85% of runtime
→
🔥 HOT
Move-To-Front
move_to_front
builds 4 new
lists per
symbol
dominant alloc churn
→
COOL
RLE Decode
Run-length
expansion
once per
block
not dominant
→
COOL
Inverse BWT
Burrows-Wheeler
inverse transform
once per
block
not dominant
🎯 Hardware accelerator scope — TWO components
(A) Bit Reader + Huffman Decode — f = 43.55% → ~1.77× alone
(B) Move-To-Front (MTF) unit — adds ~10.3% → combined f = ~53.8% → ~2.16× overall
(A) and (B) chain on-chip — Huffman symbols feed directly into MTF index, CPU not in between.
RLE and inverse-BWT (~46%) stay in software — the next accelerator candidates.
SW optimizations target
all 3
hot stages fixed
in software first

## Slide 15
THREE TARGETED FIXES — OUTPUT BYTE-IDENTICAL
pyflate — Optimizations
OPT-2 — BIGGEST WIN ⭐
In-place Move-To-Front
0 allocations instead of 4 per symbol
# AFTER: in-place, zero new lists v = l[c]; del l[c]; l.insert(0, v)
# BEFORE: 4 new lists per symbol l[:] = l[c:c+1] + l[0:c] + l[c+1:]
Example: ['a','b','c','d'] , idx=2 → output 'c' , list → ['c','a','b','d']
Before: 4 new list objects allocated. After: 0.
OPT-1
Buffered Bit Reader
Array index instead of a file call per byte
# AFTER: index preloaded buffer byte = self.data[self.pos] self.pos += 1
# BEFORE: file call PER byte c = self.f.read(1) byte = ord(c)
Example: bytes A B C → Before: f.read(1) + ord() per byte. After: data[0] , data[1] , data[2] .
OPT-3
Table-driven Huffman
O(N) scan
→
O(1) lookup
# AFTER: O(1) lookup sym, length = self.lookup[peek]
# BEFORE: O(N) scan per symbol for entry in self.table: if self.snoopbits(entry.len) == entry.code: ...
Example: codes 0→A, 10→B, 11→C. Peek 2 bits= 10 → lookup[2]=(B,2) . Before: scan all entries.
All three fixes are applied to the VM-installed pyperformance source. Algorithm and every other line of the decoder (BWT, RLE, block structure) is byte-for-byte unchanged. Correctness verified by MD5 on both sides.

## Slide 16
WALL-CLOCK SPEEDUP
~33%
1.50× · 17.6 s → 11.7 s (n=60)
vs. 7% threshold
4.75× above target ✓
MD5: afa004a630fe072901b1d9628b960974
399,360 bytes · byte-identical ✓
OPTIMIZATION SUMMARY
FIX | BEFORE | AFTER
MTF (OPT-2) | 4 new lists / symbol | 0 new lists
Bit reader (OPT-1) | file call / byte | buffer index
Huffman (OPT-3) | O(N) linear scan | O(1) table lookup
Speedup | 1.00× | 1.50×
Wall-clock | 17.6 s ± 1.3 s | 11.7 s ± 0.9 s
Combined with nbody: two benchmarks each independently past 7% → the project's "≥7% on ≥2 benchmarks" criterion is met.

## Slide 17
PART 4 — HARDWARE
Co-design Rule
🔒
Don't break user code
Python API unchanged. Same function signatures. The accelerator is an implementation detail.
↔️
Keep the public API
Same names, same argument types, same return values. A drop-in replacement.
💻
CPU fallback path
If HW absent → fall back to the optimized SW path transparently.
What we accelerate (pyflate · 2 components)
(A) Bit reader + Huffman decode — f=43.55%
(B) Move-To-Front (MTF) unit — adds ~10.3%
Combined: ~53.8% → ~2.16× overall (Amdahl est.)
HW/SW interface
AXI4-Lite control registers (MMIO)
AXI4-Stream byte-in / symbol-out DMA

## Slide 18
pyflate — Accelerator Block Diagram
SYSTEMVERILOG · INTEGER-ONLY · FULLY SYNTHESIZABLE
HUFFMAN_ACCEL + MTF_UNIT — CHAINED ON-CHIP
AXI4-Lite
(MMIO)
⇄
load tables / MTF init
▼
byte stream
(DMA in)
⟹
bit_valid
⟹
sym index
⟹
osym_valid
⟹
MTF symbols
(DMA out)
Control
CTRL
NSYM
STATUS
COUNT
TBL_CNT
TBL_SYM
MTF_N
bit_buffer
8-bit MSB-first
1 bit/cycle out
huffman_decoder
code/first/index FSM
cnt[] + symbol[] RAMs
mtf_unit
N-entry reg file
shift-to-front
1 sym/clock
(A) Huffman: code|=bit → emit symbol[index+(code−first)] · (B) MTF: out=tbl[idx]; shift tbl[idx] to front · chained on-chip, no CPU between
⚙️ Parameters
MAXLEN = 15 · SYMW = 9
MAXSYM = 512 · integer-only
📐 Area
cnt RAM ~15×16b
symbol RAM ~512×9b · very small
⚡ Frequency
300–600 MHz target
integer critical path · high fmax
🚀 Throughput
~1 bit/cycle
~60M symbols/s @ 500 MHz

## Slide 19
INTEGRATION · TRADE-OFFS
HW/SW Interface & Trade-offs
SOFTWARE DRIVER FLOW
1.
Load cnt[] / symbol[] tables via MMIO (built from code lengths pyflate already parses)
2.
Write NSYM , pulse CTRL.start
3.
DMA compressed bytes → byte_in stream
4.
DMA decoded symbols ← osym stream
5.
MTF / RLE / inverse BWT stay in SW (or become follow-on stages)
A CPython C-extension replaces pyflate's per-symbol decode loop. Public pyflate.decompress() API unchanged.
MMIO REGISTER MAP
ADDR | NAME | MEANING
0x0 | CTRL | bit0 = start pulse
0x1 | NSYM | symbols to decode
0x2 | STATUS | busy / done flags
0x3 | COUNT | symbols decoded so far
0x4 | TBL_CNT | load cnt[len] table
0x5 | TBL_SYM | load symbol[] table
Frequency
300–600
MHz (integer)
Throughput
~60M
symbols/s @ 500 MHz
SW rate
~19K
symbols/s (Python)
(A) derivation: 500 MHz ÷ ~8 bits/sym ≈ 60M sym/s HW · 148,271 sym ÷ 7.67 s ≈ 19,300 sym/s SW · sA = 60M ÷ 19.3K ≈ 3,100×
Speed/area knob: a lookup-table front end (peek MAXLEN bits → 1 symbol/cycle) costs 2^MAXLEN table RAM. A two-level table (like zlib) is the production compromise. The serial FSM here is the smallest, always-correct baseline.

## Slide 20
COMPONENT (B) · HARDWARE TWIN OF OPT-2
MTF Unit — Move-To-Front
WHAT IT DOES
An N-entry register file. Each clock:
① Output tbl[idx] ② Shift it to front
→ 1 symbol/clock · zero allocation
WORKED EXAMPLE
tbl: [10, 20, 30, 40, …] idx=2
→ output = 30
→ tbl: [30, 10, 20, 40, …]
INTERFACE
in: idx (from Huffman decoder)
out: sym (MTF-decoded symbol)
ctrl: MMIO — MTF_N, start/done
chain: Huffman osym → MTF idx (on-chip)
Why HW? SW OPT-2 fixed allocation churn. HW goes further: 1 sym/clock, register-file shift vs. Python del+insert.
Simulation
TB PASS: MTF decoded {30,30,60}
mtf_unit.sv + tb_mtf.sv · Icarus Verilog
MTF_UNIT.SV — SHIFT-TO-FRONT
sym <= tbl[idx]; // output for (int i = 0; i < N; i++) if (i == 0) tbl[0] <= tbl[idx]; else if (i <= idx) tbl[i] <= tbl[i-1];
1 symbol/clock · register-file shift · zero allocation
(B): 500 MHz × 1 sym/clk = 500M sym/s HW · 92,803÷1.81s ≈ 51K sym/s SW · sB ≈ 9,800×
Amdahl: MTF adds ~10.3% → f = 53.85% → ~2.16× overall

## Slide 21
MTF Unit — Internal Block Diagram
COMPONENT (B) · INTEGER-ONLY · 1 SYMBOL/CLOCK · CHAINS FROM HUFFMAN
MTF_UNIT — TOP LEVEL
AXI4-Lite
(MMIO)
⇄
load alphabet once per block
▼
idx (from Huffman)
in_valid / idx
⟹
out_valid / sym
⟹
sym (DMA out)
decoded symbol
Control
MTF_N
CTRL
STATUS
ld_we
ld_addr
ld_data
N-entry Register File
tbl[0]
tbl[1]
tbl[idx]
…
tbl[N-1]
Each entry: tbl[i] ← (i==0) ? tbl[idx] : (i≤idx) ? tbl[i-1] : tbl[i]
Gated by i ≤ idx — shift-to-front in one clock
Each clock: (1) output tbl[idx] · (2) shift entries 0..idx-1 right by 1 · (3) write tbl[idx] to tbl[0] · 1 symbol/clock · integer-only · no allocation
⚙️ Parameters
N = alphabet size (bzip2: up to 256) · integer-only · no FP · fully synthesizable
🔗 Load port
ld_we / ld_addr / ld_data — load the alphabet once per block over MMIO before streaming begins
🔗 Chain
Huffman osym → MTF idx directly on-chip. No CPU round-trip between components.
📐 Area
N registers + N 2:1 muxes + comparator · very small · high fmax (integer only)

## Slide 22
HUFFMAN_DECODER FSM · SPEED VS AREA TRADE-OFF
Accelerator — FSM & Trade-offs
CANONICAL DECODE FSM — 4 STATES
IDLE
Waiting for start pulse · resets code=0, first=0, index=0, len=1
start pulse
▼
DEC
Per cycle: code|=bit · compare (code−first) vs cnt[len]
if match → EMIT · else advance len
code−first < cnt[len]
▼
EMIT
Output symbol[index+(code−first)] · wait osym_ready · restart DEC or → DONE
decoded_count == nsym
▼
DONE
nsym symbols decoded · assert done · return to IDLE on next block
SPEED VS AREA TRADE-OFF
VARIANT | THROUGHPUT | TABLE RAM | STATUS
Serial FSM this design | ~1 bit/cycle ~60M sym/s | ~15×16b + ~512×9b tiny | ✓ Implemented TB PASS
Full LUT faster variant | 1 symbol/cycle ~500M sym/s | 2^15 × 13b = 53KB RAM | Design option (not built)
Two-level LUT zlib approach | ~1 symbol/cycle near-optimal | root + sub-tables much smaller | Production compromise
Note: OPT-3 in software IS the software analogue of the Full LUT variant — precomputed lookup table, one array index per symbol. The serial FSM is the smallest, always-correct hardware baseline.
HUFFMAN_DECODER.SV — S_DEC STATE (THE PER-BIT DECODE STEP)
// each clock: fold in one bit, test "code complete at this length?" code_v = code | bit_in; if ((code_v - first) < cnt[len]) // found sym <= symbol[index + (code_v - first)]; // → emit else begin // advance to next length index <= index + cnt[len]; first <= (first + cnt[len]) << 1; code <= code_v << 1; len <= len + 1; end
1 bit/clock · integer compare + add · fully synthesizable

## Slide 23
AMDAHL'S LAW · DESIGN PROPOSAL ESTIMATE · TWO COMPONENTS
Hardware Performance Estimate
f measured — cProfile on original decoder
Bit-reading: 27.70%
·
Huffman: 15.85%
·
MTF: ~10.3%
Component (A) — Huffman + bit reader
fA = 43.55% · sA ≈ 3,100× (500MHz÷8bits/sym=60M sym/s HW · 19.3K sym/s SW)
→ 1/((1−0.4355)+0.4355/3100) ≈ 1.77×
Component (B) — MTF unit added
fA+B = 53.85% · sB ≈ 9,800× (500MHz×1sym/clk=500M sym/s HW · 51K sym/s SW)
→ 1/((1−0.5385)+0.5385/s) ≈ ~2.16×
Both s values are huge → result is capped by f, not s
sA→∞: 1/(1−0.4355) = 1.77× (same) · sA+B→∞: 1/(1−0.5385) = ~2.16× (same ceiling) · Remaining ~46% (RLE + inverse-BWT) = next stage
COMPONENT (A) ALONE
~1.77×
Huffman + bit reader · f=43.55%
↓ add MTF
COMPONENTS (A) + (B)
~2.16×
+ MTF unit · f=53.85%

## Slide 24
ICARUS VERILOG · IVERILOG -G2012
RTL Simulation — Passes
COMPONENT (A) — PYFLATE HUFFMAN DECODE ENGINE
iverilog -g2012 -o sim bit_buffer.sv huffman_decoder.sv tb_huffman.sv && vvp sim
TB PASS: decoded {0,2,1} == {0,2,1}
3-symbol canonical code · hand-built table · verified decode sequence · zero mismatches
COMPONENT (B) — MTF UNIT
iverilog -g2012 -o sim mtf_unit.sv tb_mtf.sv && vvp sim
TB PASS: MTF decoded {30,30,60}
N-entry register file · shift-to-front · 1 symbol/clock · zero allocation · verified output sequence
Note on scope: An nbody N-body Processing Element (9-stage pipelined FP datapath, AXI4-Lite + AXI4-Stream, TB PASS: 5 pairs checked, 0 mismatches ) was also designed and simulated — archived under _archive/hardware_nbody/ . Per the project spec, hardware acceleration is required for at least one benchmark; the graded HW deliverable for this submission is the pyflate Huffman engine.

## Slide 25
FINAL RESULTS · KEY LESSONS
Results Summary & Takeaways
BENCHMARK | SW OPTIMIZATION | SW SPEEDUP | VS. 7% TARGET | HW STATUS
nbody | Scalar locals | ~37% | 5.2× above ✓ | SW only · nbody PE archived
pyflate | Buf + MTF + LUT | ~33% | 4.75× above ✓ | 2× TB PASS ✓ · ~2.16× est.
pyperf compare_to
nbody_orig 3.93s → nbody_opt 2.50s : 1.58x faster
pyperf compare_to
pyflate_orig 17.6s → pyflate_opt 11.7s : 1.50x faster
🔬
Measure first, always
The sqrt idea seemed right. 2.5% of runtime. Profiler said no. Trust the profiler.
⚡
SW register allocation
LOAD_FAST vs BINARY_SUBSCR. Allocation-free MTF. Same idea: keep hot data out of the heap.
💾
Amdahl caps the gain
f=53.85% → ~2.16× ceiling (Huffman + MTF). Even infinite HW can't beat 1/(1−f). Next: inverse-BWT / RLE.
🔗
Co-design payoff
The same ops hot in Python (bit reads + Huffman) map to a tiny integer FSM. SW and HW tell the same story.

## Slide 26
SUBMISSION DELIVERABLES · VERSION CONTROL
Git Repo & Documentation
📄 Reports
report_nbody.txt — overview, profiling, optimization, HW proposal
report_pyflate.txt — overview, profiling, optimization, HW proposal
🔧 Scripts
script_nbody.sh — setup, baseline, profile, optimize, compare
script_pyflate.sh — setup, baseline, profile, optimize, compare
00_setup.sh — one-time QEMU guest environment setup
💾 Hardware
hardware/pyflate/ — bit_buffer.sv, huffman_decoder.sv, huffman_accel.sv, tb_huffman.sv
hardware/pyflate/ — mtf_unit.sv, tb_mtf.sv
_archive/hardware_nbody/ — nbody PE (archived)
📋 README.md
Repository structure · how to run each script · how to reproduce results · environment requirements
🤖 prompt.txt
All AI tool prompts used (ChatGPT, GitHub Copilot) — required submission condition per the project spec
📊 Results
results/nbody_compare.txt
results/pyflate_compare.txt
results/nbody_correctness.txt
results/*.svg — flame graphs

## Slide 27
Thank You
Questions?
nbody: 1.58× / ~37% faster
pyflate: 1.50× / ~33% faster
HW: 2× TB PASS · ~2.16× est.
Both ≥7% ✓
Backup slides available: full code diffs · perf report tables · cProfile raw output · nbody archived PE design

## Slide 28
BACKUP · DEEP Q&A · FULL RAW DUMP
Raw Profiling — Full Dump
PYFLATE CPROFILE — F = 43.55% DERIVATION
ncalls tottime function 1 8.410 decode_huffman_block 148271 5.686 find_next_symbol ← Huffman 15.85% 156708 3.710 readbits ← bit-reading 92803 3.704 move_to_front 341601 3.434 snoopbits ← bit-reading 655017 2.071 _mask ← bit-reading 1 1.497 bwt_reverse 1 1.305 bwt_transform 67562 1.184 _read 67562 1.100 _more ← bit-reading 67526 0.532 needbits ──────────────────────────────────────────────────── bit-reading total : 9.961 s (27.70%) huffman decode : 5.699 s (15.85%) COMBINED f (A) : 15.660 s (43.55%) move_to_front : 3.704 s (~10.3%) ← f(B) COMBINED f (A+B) : ~53.85%
NBODY PERF TOP HOTSPOTS
Overhead Symbol 35.02% _PyEval_EvalFrameDefault ← interpreter loop 7.31% PyFloat_FromDouble 5.00% binary_op1 4.83% [unknown bucket] 4.61% float_dealloc 3.69% PyNumber_AsSsize_t 3.44% _Py_CheckSlotResult 3.01% _Py_Dealloc 2.50% __ieee754_pow_sse2 ← the ** -1.5 op 2.33% float_mul 2.27% list_subscript ← list indexing 2.03% list_ass_subscript ← v1[0] -= … 1.84% PyNumber_AsSsize_t 1.54% float_add 1.53% float_sub ──────────────────────────────────────────────────── FP ops (mul+add+sub) each only ~1.5-2.3% pow only 2.5% → sqrt swap gave ~0-1.5%